## Slide 1: CISCO Switch Configuration
Prepared by: Fahad Burhan Ahmad

## Slide 2: Cisco switch configuration steps (Set password)
Switch> //Switch will by default open in user mode//
Switch>enable //convert to privilege mode//
Switch# //Now you are in privilege mode//
Switch#show run //Show settings or changes that you made//
Now we need to set password on switch. Therefore we need to move for global mode
Switch#configure terminal //Move to configuration or global mode//
Enter configuration commands, one per line. End with CNTL/Z.
Switch(config)#line con 0
Switch(config-line)#password 123
Switch(config-line)#login
Switch(config-line)#exit
Switch(config)#exit
Switch#
%SYS-5-CONFIG_I: Configured from console by console
Switch#exit

## Slide 3: Cisco switch configuration steps (Set password)
Need to secure password we must convert the password into cypher text.
Switch>enable
Switch#configure terminal
Enter configuration commands, one per line. End with CNTL/Z.
Switch(config)#service password-encryption
Switch(config)#exit
Now you need to check either password is converted to cypher text or not
Switch>enable
Switch#show run

## Slide 4: Cisco switch configuration steps (remove password)
How to remove password from Console port
Switch>enable
Switch#configure terminal
Enter configuration commands, one per line. End with CNTL/Z.
Switch(config)#line con 0
Switch(config-line)#no password
Switch(config-line)#login
% Login disabled on line 0, until 'password' is set
Switch(config-line)#
Now check it either password is removed or not
Switch(config-line)#exit
Switch(config)#exit
Switch#exit
Switch>enable
Switch#show run

## Slide 5: Thank You
Repeat the slides until you learn